This completed form, and associated rack weight and balance information, is due to the AIC by Monday, July 20, 2009 for the CalNex project.

I.  General information:

1.  Mission name:  SENEX

2.  Instrument name: NOAA Single Particle Soot Photometer (SP2)

3.  What is measured: Refractory Black Carbon Aerosol mass, optical size, and mixing state

4.  Short description of measurement technique:  A continuous, internal, and intra-cavity IR laser is used to heat the light-absorbing and refractory carbon components of aerosol particles < 1 µm in diameter to vaporization.  The light scattered out of the laser, as well as thermal emissions from the hot particle are recorded.  In post-processing this data is interpreted for black carbon composition, mass, optical size, and mixing state.

5. Contact information for all personnel going to the field with this instrument:

(for multiple investigators, please list the PI or primary contact person first)

| Name | Email | Office phone | Cell phone |
| --- | --- | --- | --- |
| 1. Joshua (Shuka) Schwarz | Joshua.p.schwarz@noaa.gov | 3034974637 | 303-5061-892 |
| 2. Milos Markovic | Milos.markovic@noaa.gov | 303 497 3244 | 720 470 3041 |

I.  Specific information:

1. Total installed weight:	155 lbs

(rack, gas cylinders, hoses, cabling, pumps, inlets, permeation tubes, etc.)

| Rack weight and balance info | Allowed | Actual |
| --- | --- | --- |
| Weight, lbs.: |  | 135 lbs (approximate) |
| Overturning moment, in-lbs.: |  | 3100 in-lb (approximate) (split between in/outboard rack half) |

Pod weight and CG:

NOTE: Please also provide weight-and-balance information for all installed equipment.  Templates for standard electronics racks are available for download here.  PIs with non-standard installations will need to provide relevant information in a similar format.

2.  Individual subassembly info (weights should sum to total listed above)

| Component name | Location name and flight station | Weight, lbs |
| --- | --- | --- |
| 1.Computer and pump | S-3 Rack, outboard | 55 |
| 2. SP2 detection box/mount | S-3 Rack | 80 |
| 3. |  |  |
| 4. |  |  |
| 5. |  |  |
| 6. |  |  |

3.  Component power consumption in Amps

| Component name | Location name | 400 Hz 3Ø | 400 Hz 1Ø | 60 Hz | 28VDC | 28VDC WOW |
| --- | --- | --- | --- | --- | --- | --- |
| 1. SP2 (one power tap) | S-3 rack | - | - | 5 | 0 | 0 |
| 2. |  |  |  |  |  |  |
| 3. |  |  |  |  |  |  |
| 4. |  |  |  |  |  |  |
| 5. |  |  |  |  |  |  |
| 6. |  |  |  |  |  |  |
| 7. |  |  |  |  |  |  |
| 8. |  |  |  |  |  |  |
| 9. |  |  |  |  |  |  |
| 10. |  |  |  |  |  |  |
| 11. |  |  |  |  |  |  |
| 12. |  |  |  |  |  |  |
|  | Totals: |  |  |  |  |  |
|  |  | 400 Hz 3Ø | 400 Hz 1Ø | 60 Hz | 28VDC | 28VDC WOW |

4.  Inlet and exhaust information:

| Inlet/exhaust name | Location name and flight station | Hole size through hull, inches |
| --- | --- | --- |
| 1. LTI – common line | FD window, FS 309 | 2.5 |
| 2. No exhaust port required |  |  |
| 3. |  |  |
| 4. |  |  |
| 5. |  |  |
| 6. |  |  |

5.  Source of flow (name and location of pump or venturi)

| Pump name | Location name and flight station |
| --- | --- |
| 1. KnF N920 diaphragm pump | Station 3 Rack |
| 2. |  |
| 3. |  |
| 4. |  |
| 5. |  |
| 6. |  |

6.  Installed hazardous materials or equipment:

(only for items installed in the aircraft for use during flight)

A.  Lasers

Type:  CW diode

Class:  1 (embedded)

Wavelength:  808 nm

Output power:  2 W

Eye-safe?  Yes (fully contained)

Beam fully contained within instrument during normal operation?  Yes

Type: CW Nd-YAG

Class: 1 (embedded)

Wavelength: 1.06 µm

Output power: 50 mW

Eye-safe? Yes (fully contained)

Beam fully contained within instrument during normal operation?

Yes.

For non-eye-safe lasers, please attach a description of safety measures taken (safety interlocks, beam fully enclosed within instrument, etc.) and a procedure for safe instrument operation during testing and laser alignment.  Please contact the AIC for an example of laser safety documentation from TexAQS 2006.

B.  RF transmitters:  (note that mass spectrometer RF generators are not designed to transmit, and do not need to be included here)

Description: None

Transmitted RF power:

Frequency range:

C.  Radioactive materials:

Isotope: None

Half-life:

Type of emitter:

Generally licensed?

# installed and location:

# of spares and location:

D.  Compressed gases: (1 ft3 = 28.32 liters; cabin volume = 4260 ft3 = 1.21 x 105 liters)

| Cylinder number: | 1 | 2 | 3 | 4 | 5 |
| --- | --- | --- | --- | --- | --- |
| Gas description | None |  |  |  |  |
| Mixing ratio |  |  |  |  |  |
| Cylinder size (ft3) |  |  |  |  |  |
| Max pressure (psig) |  |  |  |  |  |
| # installed on aircraft |  |  |  |  |  |
| Location on aircraft |  |  |  |  |  |
| Service frequency |  |  |  |  |  |
| toxic/flammable gases: |  |  |  |  |  |
| In containment vessel? |  |  |  |  |  |
| Gas alarm provided? |  |  |  |  |  |
| MR if vented to cabin, ppmv |  |  |  |  |  |
| OSHA 8-hr PEL, ppmv |  |  |  |  |  |
| 30-min IDLH, ppmv |  |  |  |  |  |

E.  Chemicals (solids and liquids):

| Chemical number: | 1 | 2 | 3 | 4 | 5 | 6 |
| --- | --- | --- | --- | --- | --- | --- |
| Concentration | None |  |  |  |  |  |
| Amount |  |  |  |  |  |  |
| Container description |  |  |  |  |  |  |
| Purpose |  |  |  |  |  |  |
| Solution pH |  |  |  |  |  |  |
| Spill kit provided? |  |  |  |  |  |  |

F.  Cryogens:

Location: None

Description:

Container description:

Quantity on board per flight:

Serviced on the aircraft?

G.  UPS and battery installation:

Location: None

Description:  (Manufacturer, model no., power)

Battery type:

Has an adjustable input voltage tolerance? (highly recommended)!

H.  Motors

Description: Brushless DC motor for the pump

Motor current draw  24V, 5A startup, 2A running

(e.g., 3Ø, 400Hz, 8A startup, 4A running)

Thermal interlock enabled? No

Operator seat requests -

Test flights: None

Transit flights: None

Science flights: None

7.  Data and plumbing drops

Network (Cat. 5/6 ethernet) drops requested:

Serial drops requested:

IRIG-B drops (BNC coax connector) requested:

Vacuum/exhaust/ emergency dump lines:

| Name | Flow rate, slpm | Line pressure, Torr | Pump type | Trace gas concentration(s) |
| --- | --- | --- | --- | --- |
| 1. |  |  |  |  |
| 2. |  |  |  |  |
| 3. |  |  |  |  |
| 4. |  |  |  |  |

Ground gas service lines (number, location, type of service):

Other gas lines (number, location, type of service):

Will you be sending data to the AOC data station?  If so, please provide the following information:

| Parameter name | Voltage range | Unit conversion |
| --- | --- | --- |
| 1. |  |  |
| 2. |  |  |
| 3. |  |  |

8.  Aircraft access

a.  flight days:

Pre-flight time requested at aircraft (hours): 1

Routine pre-flight ground support required?  No

(stands, ladders, forklifts, covers, external equipment, etc.)

Routine post-flight time requested at aircraft (hours):  1

Routine post-flight ground support required?  No

(stands, ladders, forklifts, covers, external equipment, etc.)

b.  non-flight days:

Routine external access to inlets or zenith mounts required? No

(please describe location, how often, for how long, type of ground support equipment needed, weather constraints, etc.)

Please note there is zero access and zero power to the aircraft (including pods) on hard-down days.  These occur at least once every seven calendar days while in the field.

9.  Aircraft maneuvers

Briefly describe in-flight calibration frequency, duration, altitudes desired: None

Briefly describe instrument sensitivity to flight conditions: Possible cloud particle contamination of inlet

(issues during roll/pitch, ascent/descent, sampling in cloud, icing etc.)

10.  Miscellaneous

1.  Hazmat for preflight/postflight calibrations:  Please describe fully any additional hazardous materials - compressed gases, solvents, radioactive ion sources – that you anticipate temporarily bringing onto the aircraft for periodic instrument calibration purposes  (e.g., n-butanol in a CN counter, 210Po in a DMA, a UPS for power, compressed gas cylinders for calibrations, etc.)

None.

2.  Fabrication and sheet metal support:  Please describe fully any anticipated requests for fabrication or sheet-metal support during installation in Tampa.  This list should be kept to an absolute minimum; please recognize that this superb AOC resource is quite limited.  To ease the strain on the AOC shop, we will work with each PI to ensure they arrive in Tampa with as much in hand as possible.

None.

3.  Ferry flight/check flight procedures.  On occasion, AOC will perform an aircraft check flight, during which the instruments may be flown without power.  Aircraft maintenance needs may also dictate a ferry flight without science crew or SED techs on board.  Instruments should be designed with these eventualities in mind.  However, if your instrument requires standby power during this kind of flight, this may be provided at the discretion of AOC personnel.

If so, the flight crew will need to be briefed well ahead of time to ensure proper instrument operation.  Please provide with this document a bare-minimum checklist of instrument startup and shutdown procedures requested for these flights.

No special requirements.

II.  Ground laboratory space

1.  Tampa space requests:

Power requirements:

Special requests:

None.

2.  Field space requests:

Workspace, ft2: 200

Number of tables/chairs: 2/4

Power requirements: 60Hz, 2 kW

Storage space, ft2: 50

Other requests: Internet access