Right-click on Connections, in the Workspace window in DaqFactory, to create a new connection. Enter an arbitrary name, then enter the IP address from the list below; passwords are not required (the connection name can be anything that makes sense to you; the IP address fully specifies the remote computer).  Verify that “Full Stream” is NOT checked. (This will reduce the amount of traffic on the network, and will only display channels deliberately broadcast from each instrument).

ConnectionName	IP address		ChannelName			Conversion		Units		PI

Update prior to transit

NOyO3		10.10.16.202		NO_counts			(x-800)/5.5OLD	ppbv		Tom/Steve

NOy_counts			(x-800)/5.5OLD	ppbv

O3_counts			(x-200)/2.5OLD	ppbv

CO2CH4		10.10.16.204		CO2_ppmv_serial		(x/0.3)OLD		ppmv		Jeff

CH4_ppmv_serial					ppmv 		Jeff

Ethane_ppbv_serial?					ppbv? 		Jeff

CO			10.10.16.213		C00_pmt0			(x-1500)/29OLD	ppbv		John H.

SO2			10.10.16.207		SO2_C01_fluor_int					ppbv		John H.

NMASS		10.10.16.210		counter1			(x1013/(90*4.5) OLD	#/cc		Chuck

FliSci			10.10.16.200		AOC_GpsLat						degrees	Ken

(subset shown)	AOC_GpsLon						degrees

AOC_GpsAlt						meters

AOC_Palt						feet

AOC_Ralt						meters

AOC_AmbTemp					°C

AOC_DewPtTemp					°C

AOC_H2Omr						g/kg (parts per thousand by weight)

AOC_StaticPrs					millibar

AOC_DewPtTempTDL				°C

AOC_WindDir					degrees

AOC_WindSpd					m/s

AOC_CabinPrs					millibar

AOC_GndSpd						m/s

AOC_Heading						degrees

ConnectionName	IP address		ChannelName			Conversion		Units		PI

FliSci	(cont.)		10.10.16.30		AOC_ACES_NO2					ppbv		Kyle

FliSci	(cont.)		10.10.16.30		AOC_ACES_Gly					ppbv		Kyle

AOC_ NOxCARD_NO2				ppbv		Rob

AOC_ NOxCARD_NOx				ppbv		Rob

AOC_ NOxCARD_Ox				ppbv		Rob

AOC_NOxCARD_NOy				ppbv		Rob

AOC_iWAS_Time					hhmmss	Brian

AOC_iWAS_CanNum				#		Brian

AOC_iWAS_ManPres				mb		Brian

Use “ConnectionName.ChannelName” to call these remote channels in your copy of DF.  For example, to display Chuck’s small particle data, add a trace called “NMASS.counter1” to your graph.

Note that it sometimes takes several attempts to successfully connect to the remote copy of DF.  Left-click on the connection name in the Workspace window, and click on “reset connection” until the Packets Received counter begins to increment and channels on remote computer are listed.