## Slide 1
Absorption by ambient aerosols during CalNex
Chris Cappa (UCD)
Paola Massoli
Tim Onasch
Doug Worsnop
Katheryn Kolesar
Jani Hakala
Shao-Meng Li
Ibraheem Nuaaman
Kathy Hayden
Trish Quinn
Tim Bates
Dan Mellon
and more…
CaLNex
A
t
n
t
i
s
l

## Slide 2
Aerosol Volatility and Optical Properties
[Lack and Cappa, ACP, 2010]
Light absorption by particles from black carbon (soot) and brown carbon
Coatings on BC can theoretically enhance absorption in climatically important ways
[e.g. Jacobson, Nature, 2001]
Enhancement factor can be calculated from Mie theory, but limited validation from ambient measurements
Objective: to directly measure the absorption enhancement factor for ambient particles at multiple wavelengths

## Slide 3
Ambient
Really hot
Large Enhancement
Small Enhancement
Highly Scattering
Less Scattering
Brown Carbon
No Brown Carbon
Absorption by brown carbon should contribute more to total absorption at short l
Approach: Heat Particles to Drive Off Coatings

## Slide 5
Measurements
Thermo-
denuder
HR-ToF-AMS
SP-AMS
PAS/CRD
SMPS
SP2
MAST
or
Note: PM1 cutoff
Non-refractory particle composition
BC & coating composition
Particle absorption & extinction
Size Distribution
BC mass distribution
Env. Ca
Aerodyne
UC Davis
Env. Ca
Env. Ca
PAS/CRD measures light absorption and light extinction at 532 nm and 405 nm
SP-AMS measures BC mass and coating composition
SP2 measures BC mass and infers coating thickness
SP2 and SPAMS tell us something about how coating thickness has changed upon heating
SP2 BC measurement can tell us about particle losses through the TD

## Slide 6
Particle Transmission Correction
Similar results to Huffman et al. (2008): Tr = 0.98 – 0.00082*Temp

## Slide 7
Influence of heating on particle extinction (532 nm)
Black = ambient
Red = denuded

## Slide 8
Influence of heating on particle extinction

## Slide 9
Lines are binned data over different time periods
Total aerosol volatility varies greatly with time/location
Very similar results from SMPS
Influence of heating on particle extinction
Start of Campaign
End of Campaign

## Slide 10
Influence of heating on particle absorption
Note: only include periods when
babs,ambient > 0.5 Mm-1
532 nm
405 nm

## Slide 11
Influence of heating on particle absorption
532 nm
405 nm

## Slide 13
Theoretical Calculations of Aerosol Optical Properties
Use “core-shell” Mie theory to calculate evolution of sabs, sext and SSA
Dp(particle) = 400 nm
Dp(core) = 80 nm
sabs = 9.8 x 10-15 m2/particle
sext = 2.9 x 10-13 m2/particle
SSA = 0.97
Dp(particle) = 100 nm
Dp(core) = 80 nm
sabs = 3.8 x 10-15 m2/particle
sext = 4.4 x 10-15 m2/particle
SSA = 0.13
Dp(particle) = 200 nm
Dp(core) = 60 nm
sabs = 2.9 x 10-15 m2/particle
sext = 1.5 x 10-14 m2/particle
SSA = 0.81
Dp(particle) = 120 nm
Dp(core) = 60 nm
sabs = 2.0 x 10-15 m2/particle
sext = 2.8 x 10-15 m2/particle
SSA = 0.16
Eabs = 2.57
FRext = 0.015
DSSA = 0.84
Eabs = 1.45
FRext = 0.19
DSSA = 0.65

## Slide 14
Model: Mie Core-Shell
Dp = 250 nm
SSAi = 0.95; Dcore = 50 nm

## Slide 15
Model: Mie Core-Shell
Dp = 250 nm
SSAi = 0.95; Dcore = 50 nm
SSAi = 0.88; Dcore = 70 nm
SSAi = 0.77; Dcore = 90 nm
SSAi = 0.67; Dcore = 110 nm

## Slide 16
Model: Mie Core-Shell
SSAi = 0.95
SSAi = 0.88
SSAi = 0.77
SSAi = 0.67; vary Dp
SSAi = 0.58
Dp = 150 nm
Dp = 100 nm
Dp = 80 nm

## Slide 18
Mie “Core-Shell” Results

## Slide 19
Mie “Core-Shell” Results

## Slide 20
Since we are talking about California anyway…
same experiment done at CARES, but with fixed TD temperature (225 °C) and PM2.5
Note: variation in FRext from atmosphere, not temperature

## Slide 21
Why such an (unexpectedly) low absorption enhancement?
1. Concern: particles are not internally mixed
2. Particles are internally mixed, but not with “core-shell” morphology
+

## Slide 22
H-TDMA indicates aerosol dominated by single growth mode

## Slide 23
Dp,core = 40 nm
Dp,core = 140 nm
Points = observed
Lines = calculations

## Slide 24
SP-AMS sees only particles that contain black carbon
SSA shows similar variation with
Dp,core = 40 nm
Dp,core = 140 nm
which would only be the case if particles are internally mixed.

## Slide 25
Brown Carbon Absorption

## Slide 26
Brown Carbon Absorption
~10% of absorption at 405 nm may be due to “Brown” Carbon
Imaginary Refractive Index ~ 0.009

## Slide 27
Conclusions
Absorption enhancements much smaller than expected
Suggests internal mixtures but not with “core-shell” morphology
Absorption by “brown” carbon ~ 10% of total at 405 nm
Thanks again to all my great collaborators, the R/V Atlantis Crew and the EPA and NOAA for funding.